DIVISION 08 - OPENINGS

SECTION 08 42 29.23 SLIDING AUTOMATIC ENTRANCES

Specifier Note: Coordinate and edit articles and paragraphs below to suit project requirements. Add section numbers and titles per CSI "MasterFormat" and specifier's practice. Consult with manufacturer regarding performance requirements for units applicable to project, as well as related equipment and accessories required.

PART I – GENERAL

1.01 SUMMARY

A. 	WORK INCLUDED: Furnish specified complete automatic aluminum cleanroom door system, that has been manufactured, fabricated & installed to meet manufacturer’s standards without defects, damage, or failure.

B. 	RELATED WORK: Openings: Division 08, applicable sections.

1.02 REFERENCES

A.  AMERICAN ASSOCIATION OF AUTOMATIC DOOR MANUFACTURERS (AAADM).

B. 	AMERICAN NATIONAL STANDARDS INSTITUTE (ANSI):

1. 	ANSI Z97.1: Safety Glazing Materials Used in Buildings - Methods of Test.

2. 	ANSI A156.10: For Power Operated Pedestrian Doors; Sliding Doors section.

3.	ANSI A156.5: Standard for Auxiliary Locks and Associated Products

C. 	AMERICAN SOCIETY FOR TESTING AND MATERIALS (ASTM) B221: Aluminum-Alloy Extruded Bars, Rods, Shapes and Tubes.

D. 	BUILDING OFFICIALS AND CODE ADMINISTRATORS INTERNATIONAL (BOCA)

E.	INTERNATIONAL CONFERENCE OF BUILDING OFFICIALS / UNIFORM BUILDING CODE (ICBO/UBC)

F.	International Code Council / International Building Code (ICC/IBC)

G.	INTERNATIONAL ORGANIZATION FOR STANDARDIZATION (ISO) 14644, Class 5: Cleanrooms & Associated Controlled Environments, Classification of air cleanliness by particle concentration.

H. 	NATIONAL FIRE PROTECTION ASSOCIATION (NFPA) 101: Safety to Life from Fire in Buildings & Structures.

I. 	THE ALUMINUM ASSOCIATION (AA) Aluminum Finishes Manual.

J. 	INTERTEK, WARNOCK HERSEY (ETL): Testing Laboratory and Certification Agency joined with ETL SEMKO

K. 	UNDERWRITERS LABORATORY, INC. (USA & CANADA) UL 325: Electrical Door, Drapery, Gate, Louver, and Window Operators and Systems.

1.03 SUBMITTALS

A. 	SHOP DRAWINGS & PRODUCT DATA: Submit drawings and product data showing layout, profiles, product components including anchorage, accessories, finish and glazing details (where required).

B. 	CLOSEOUT SUBMITTALS: Submit the following:

1. 	Owner’s Manual & Warranty document as specified herein.

2. 	AAADM inspection compliance form completed and signed by certified AAADM inspector prior to doors being placed in operation as proof of compliance with ANSI A156.10.

1.04 QUALITY ASSURANCE AND PERFORMANCE REQUIREMENTS

A. 	INSTALLERS QUALIFICATIONS: Installer shall be factory trained, certified by AAADM, and experienced to perform work of this section.

B. 	MANUFACTURER’S QUALIFICATIONS: Manufacturer to have minimum (5) five years successful experience in the fabrication of automatic doors of the type required for this project. Manufacturer capable of providing field service representation during installation, approving acceptable installer, and approving application method.

C.	CERTIFICATIONS: Automatic sliding door systems and options shall be factory certified to meet performance design criteria in accordance with the following standards:

1.	ANSI A156.10: For Power Operated Pedestrian Doors; Sliding Doors section.

2.	NFPA 101: Code for Safety to Life from Fire in Buildings & Structures.

3.	ETL Listed: Tested to UL 325 Standard

4.	BOCA: Means of Egress, Power Operated Doors

5.	ICBO/UBC: Egress Through Lobbies

6.	ICC/IBC: Egress Section

7.	Certificate of Compliance of ISO Class 5 Cleanroom (as determined by independent ISO 14644 testing lab)

D.	OPERATING RANGE: -30° F to 130° F (-34° C to 54° C)

E. 	OPENING FORCE REQUIREMENTS FOR Emergency Egress:

1. 	Slide-swing panels shall require no more than 50 lbf. (222 N) of force to swing open. Slide-swing panels shall be capable of swinging out 90° from any position of slide movement.

2. 	Slide-swing panels and swing-out sidelites shall have torsion spring designed to re-close panel if pushed open in the direction of egress.

3. 	If power fails, slide panels can be manually slid open with no more than 15 lbf (67 N) of force.

4. 	Units are ETL listed as an exit way and are compliant with NFPA 101.

F. 	CLOSING FORCE REQUIREMENTS: Maximum force required to prevent sliding panel from closing = 28 lbf. (124 N) Adjustable Reversing Circuit will reopen door unit if closing path is obstructed.

G.	HEADER CAPACITY: Header shall be capable of supporting:

1.	Biparting: Up to 250 lbs. (113.4 kg) per slide panel over spans up to 16’-0” (4877mm) without intermediate supports.

2.	Single Slide: Up to 250 lbs. (113.4 kg) per slide panel over spans up to 9’-0” (2743mm) without intermediate supports.

1.05 WARRANTIES

A. 	MANUFACTURER'S WARRANTY: Units to be warranted against defect in material and workmanship for a period of two years from the Date of Substantial Completion. Manufacturer's warranty is in addition to, and not a limitation of, other rights owner may have under Contract Documents.

B. 	DISTRIBUTOR'S WARRANTY: 1-year warranty: Labor & transportation charges for defective parts replacement.

1.06 PROJECT CONDITIONS

Field Measurements: Verify actual dimensions/openings by field measurements before fabrication and record on shop drawings. Coordinate with fabrication and construction schedule to avoid construction delays.

1.07 DELIVERY, STORAGE AND HANDLING

A. 	ORDERING AND DELIVERY: Comply with factory's ordering instructions and lead time requirements. Delivery shall be in factory's original, unopened, undamaged containers with identification labels intact.

B. 	STORAGE AND PROTECTION: Provide protection from exposure to harmful weather conditions and vandalism.

# PART II – PRODUCTS

2.01 MANUFACTURER

Horton Automatics, a division of Overhead Door Corporation, shall manufacture automatic cleanroom sliding door(s) of type(s) and size(s) specified on plans and door schedule.

2.02 EQUIPMENT

A. 	MANUFACTURED DOOR UNITS: Shall include operator, header with roller track, carrier assemblies, framing, sliding door panel(s), sidelite(s), activation, safety devices and accessories required for complete installation.

1.	Configuration: Single Slide or Biparting

2.	Mounting Type:

a.	Perimeter mounted within rough opening with sliding panel(s) sliding along sidelight(s).

b.	Surface mounted with sliding panel(s) sliding along wall eliminating need for sidelite.

3. 	Door Type:

a. 	Type 110: Slide-swing panel(s) ‘SX’ shall slide along exterior ‘O’ fixed sidelite(s).

b. 	Type 310: Slide-swing panel(s) ‘SX’ shall slide along interior ‘SO’ swing-out sidelite(s)

B.	OPERATOR: The Electric Operating Mechanism shall be ProSlide Series 2021 Belt Drive. Maximum current draw shall not exceed 3.15 amps. The operator shall be mounted and concealed within the header.

1. 	Operating force shall be accomplished through a 1/8 HP DC permanent magnet motor with worm gear transmission and 1800 RPM working with drive belt, attached door hangers, and idler pulley. Maximum current draw shall not exceed 3.15 amps. Drive belt to be steel reinforced nylon, 1/2" (13 mm) wide. Idler pulley to be reinforced, metallic material.

2.	Microprocessor-based control shall include a 40-character alphanumeric display to provide ease of adjustment and comprehensive diagnostics, including error and alarm logging. All speeds, forces and time delays shall be independently adjustable. Actuating and safety sensors that provide self-monitoring are supported. Supported operating modes include 2-Way Automatic / 1-Way Exit, Full / Reduced Door Opening, and Day / Night Operation.

3.  Finger Safety: Strike rail of sliding panel will stop short of adjacent sidelite; resulting opening is net slide.

4. 	On/Off Switch shall be supplied. When switched OFF, unit reverts to free manual operation (likewise during electrical power failure).

C. 	Security and Safety Power Fail Options:

1. 	Automatic lock: Automatically locks slide function of door when in closed position. Additional power supply for autolock not acceptable.

a. 	Autolock Fail Secure: If power fails the lock engages.

b. 	Autolock Fail Safe: If power fails the lock disengages.

2. 	Monitored Power Fail Options (battery back-up):

a. 	Software Selectable Power Fail Open: If power fails the door slides open.

b. 	Software Selectable Power Fail Close: If power fails the door slides closed.

D. PROSLIDE HEADER: Shall be 4 1/2" (114mm) deep by 7" (178mm) high aluminum construction with integrated extruded wire chase and extruded dovetails at top of header for transom option. Header shall have removable, self-locking face plate for service and adjustment of operator and controls.

E. 	CARRIER ASSEMBLIES AND HEADER ROLLER TRACK: Carrier assemblies shall support door panels with minimum four rollers per panel. Rollers will be non-metallic, high quality ball bearing wheels 2" (51mm) diameter. Anti-Derailing shall be accomplished by means of a Delrin block attached to carriage. Overhead header roller track shall be continuous aluminum.

F. 	SLIDING PANEL(S) AND SIDELITE(S): Shall be aluminum, 1-3/4" (44 mm) deep with narrow stile rails. Standard bottom rail shall be 4" (102mm) tall. Sliding panels shall have concealed bottom guides to stabilize slide travel.

1. 	Weather-stripping: Captured in extruded aluminum door panel. Surface applied self-adhesive weatherstripping not acceptable. Adjustable spring-loaded double astragal weather-stripping at lead edge, double neoprene at interlock rails

2.	Standard glazing prep to be for 1/4” (6 mm) glass using beveled horizontal glass stops.

3. 	Sliding Panel and Sidelite Options shall be:

a.  1" (25mm), 2 1/4" (57mm), 4" (102mm) or 6 1/2" (165mm) wide muntin (mid-rail).

b. 	6 1/2" (165mm), 8" (203mm), 10" (254mm) or 12" (305mm) tall bottom rail.

G. 	BREAKOUT PANELS: Slide-swing panels can swing out minimum 90° from any position of slide movement and require no more than 50 lbf. (222 N) of force applied at the lock stile to open. Slide-swing panels and swing-out sidelites shall utilize spring loaded ball detent.

1. 	Slide-swing panels and swing-out sidelites shall have torsion spring designed to re-close panel if pushed open in the direction of egress.

2. 	Breakout mechanism shall provide support across full width of the door, in normal operating mode. In breakout mode, torsion assembly shall support weight of the door to minimize drop during emergency egress.

3. 	Slide-swing panels shall include intermediate horizontal rail.

4. 	Units with breakout feature are ETL listed as an exit away and are compliant with NFPA 101.

H. 	JAMBS/FRAME: Aluminum jamb dimensions to be: 1 3/4" (44mm) deep by 4" (102mm) wide.

Option widths: 4 ½” (114mm) or 6” (152mm)

I. 	HARDWARE (Optional): ANSI A156.5, Grade 1, 2-Point Locking provided & installed in strike rail shall include:

1. 	Hookbolt Latch, 5/8” laminated stainless steel, latching into jamb or adjacent strike rail.

2. 	3/8” hex-bolt into breakout carrier frame.

3. 	Keyed 1 5/32" (29mm) Cylinder mounted on exterior side with 31/32" (25mm) backset

4. 	Thumbturn mounted on interior side.

2.03  RELATED EQUIPMENT

BASIC SENSOR SYSTEM: Shall be 24 VDC, class ll circuit and shall be adjusted and installed in compliance with ANSI A156.10. System shall include the following:

A. 	Activation sensors: Microwave or active infrared sensor shall be header-mounted each side of door unit for detection of traffic from each direction.

B. 	Threshold presence sensors:

1. 	Header mounted sensors shall provide active infrared presence detection on each side of the door unit and shall remain active throughout the entire door opening and closing cycle.

2. 	Hold-open beams: Two pulsed infrared photoelectric beams to be mounted in vertical rails of sidelite or in jambs. Sender/receiver arrangement parallels door opening.

3.	Touchless jamb mounted switch (optional wall mounted) using diffused scanning technology with adjustable range up to 15" (381 mm). Junction box included.

4. 	Push Plate jamb mounted switch (optional wall mounted): Momentary contact switch, stainless steel plate on standard junction box.

C. OPTIONAL INTERLOCK CONTROLLER: Multiple doors entering a clean room and/or vestibule area shall include a microprocessor-based interlock control to prevent two doors from being open at the same time. The control shall keep track of the order of request from the activation switch. Design shall control up to eight doors and shall have a memory capable of remembering order of open requests.

2.04  RELATED WORK REQUIREMENTS

A. 	ELECTRICAL: 120 VACS, 50/60 cycle, single phase, dedicated 20-amp circuit per operator. Non-North American voltages can be 240 VAC 50/60 cycle (operator must have 240-volt power supply).

B. 	GLASS AND GLAZING: Glass stops, glazing vinyl and setting blocks for field glazing as per Safety Glazing standard ANSI Z97.1.2. Contractor to coordinate acquisition of glass in thickness and type in accordance with manufacturer's recommendations for prescribed design.

2.05  MATERIALS, FINISHES AND FABRICATION

A. 	EXTRUDED ALUMINUM: ASTM B221, 6063-T5 alloy and temper, anodized:

1. 	Structural Header Sections: Minimum 3/16" (5mm) thickness.

2. 	Structural Frame Sections: Minimum 1/8" (3mm) thickness.

3.  Structural Panel Sections: Commercial grade.

B. 	FINISHES (for all exposed aluminum surfaces): Shall be one of the following:

1. 	215-R1 Clear: Architectural Class 1 Clear Anodized Coating, AA-MI2C22A41.

2. 	313-R1 Dark Bronze, 312-R1 Light Bronze, or 315-R1 Black: Architectural Class 1 Anodized Coating,

AA-MI2C22A44.

3. 	Special Powder-coat Paint Coating: Color as selected.

4. 	Clad with stainless steel or muntz metal (brass alloy): #7 mirror finish or #4 brushed finish.

C.	PANEL CONSTRUCTION:

1.	Corner block type with 3/16" steel backup plate construction, mechanically secured with minimum of four hardened steel screws. Sash consists of snap-in glass stops, snap-in glazing beads and vinyl gaskets. Gasketing material to be captured in extruded aluminum door panel.

2.	Slide-swing doors to be supplied with adjustable glass setting block to allow for adjusting of door to meet site conditions eliminating the need for additional shims.

D. 	FRAME CONSTRUCTION: Butt joints, mechanically secured by means of screws & formed aluminum brackets.

PART III - EXECUTION

3.01 EXAMINATION

Site Verification of Conditions: Installer shall verify base conditions are acceptable for product installation as per manufacturer's instructions. Notify Contractor in writing of conditions detrimental to proper & timely completion of work. All negative conditions to be corrected in a manner acceptable to the manufacturer.

3.02 INSTALLATION

A. 	GENERAL: Installer shall be factory trained, certified by AAADM, and experienced to perform work of this section. Install door units plumb, level and true to line, without warp or rack of frames or sash with manufacturer's prescribed tolerances. Provide support and anchor in place.

B. 	DISSIMILAR MATERIALS: Comply with AAMA 101, Appendix Dissimilar Materials by separating aluminum materials and other corrodible surfaces from sources of corrosion or electrolytic action contact points.

C. 	ELECTRICAL: General or electrical contractor to install all wiring to operator on a separate circuit breaker routed into header. General or electrical contractor also to install all necessary power and low voltage wiring for proper operation of associated security systems.

3.03 CLEANING, ADJUSTMENT AND PROTECTION

A. 	CLEANING: Remove temporary protection of adjacent work areas. Remove construction debris from construction site and legally dispose of debris. Repair or replace damaged installed products. Clean product surfaces and lubricate operating equipment for optimum condition and safety

B. 	ADJUSTMENT: AAADM certified technician to inspect and adjust installation. Comply with ANSI A156.10.

C. 	ADVISE CONTRACTOR: Of precautions required through the remainder of the construction period, to ensure that doors will be without damage or deterioration (other than normal weathering) at the time of acceptance.

Horton Automatics reserves the right to make product improvements and change specifications without notice.

## END OF SECTION